## Slide 1: NUMERICAL ANALYSIS ON HEAT TRANSFER ENHANCEMENT OF POROUS FIN

## Slide 2
GROUP MEMBERS
JISHNU JAYARAJ
DEEPAK RAJ A S
PRAVEEN K PRASAD
VISHNU K P
DILDEEP T C
RIYAS V
VISHNU K P
MIDHUN DAS
GUIDED BY
NAVEEN

## Slide 3: INTRODUCTION
Thermal management has become a critical aspect of today’s technology, which often include many high-performance machines and circuits that dissipate large amounts of heat. Many of these components require efficient cooling to prevent overheating.
Recent development of high performance devices has added the need for designing an efficient method for heat dissipation.
The performance of electronic system and machines deteriorates precipitously when the temperature of the devices trips beyond a certain threshold limit.

## Slide 4: FINS
Fins enhances heat transfer from a surface by exposing a larger surface area to convection and radiation.
The rate of heat transfer from a surface at temperature to the surrounding medium at is given by Newton's law of cooling as
= h ( - )
h - convective heat transfer coefficient (W/K)
- heat transfer surface area ()

## Slide 5: HEAT TRANSFER IN FINS

## Slide 6: OBJECTIVE
To develop a CFD model of rectangular fin enclosed in a air domain and then to optimize the heat transfer.
To analyze the thermal performance of fin by comparing temperature contour and velocity contour ,also to study velocity vector.
To compare results of solid fin with porous fin.

## Slide 7: SOFTWARE USED
ANSYS 16.0
GEOMETRY
the model is made in ansys design modeler.
MESHING
meshing was done in ansys 16.0 mesh tool.
SIMULATION
the CFD model was simulated in ansys fluent

## Slide 8: GEOMETRIC PARAMETERS
Fin
type : solid
length : 100mm
breadth : 50mm
height : 5mm
Air domain
type : fluid
length : 200mm
breadth : 200mm
height : 200mm

## Slide 9: GEOMETRY

## Slide 10: GRID INDEPENDENT STUDY

## Slide 11: ASSUMPTIONS AND BOUNDARY CONDITIONS
Heat flux in to the fin is given at the base of the fin. Heat flux = 24000W/m2
Operating temperature is considered as 300K.
Pressure outside the domain is considered as atmospheric (101325Pa).
Boussnnesq equation

## Slide 12: ASSUMPTIONS (CONT)
The analysis is made on a rectangular Aluminum fin having
thermal conductivity 202 W/mK
density 2719 Kg/m3
specific heat 871 J/kg K
The working fluid is air having
density 1.165 Kg/m3
dynamic Viscosity 1.84X10-5 Ns/m2
Specific heat 1005J/kgK
thermal conductivity 0.025 W/mK
thermal expansion coefficient 0.0033
Ambient temperature is considered as 300K for simulation

## Slide 13: MESH DETAILS

## Slide 14: GOVERNING EQUATION
For the fluid flow and the convective heat transfer conservation equations were taken as
Conservation Of Mass
( u)=0
Conservation Of Momentum
(u*u) = -+ [w(u + (u)T)]
Conservation Of Energy
w Cpu T = kw2T

## Slide 15: TEMPERATURE CONTOUR OF SOLID FIN

## Slide 16: VELOCITY CONTOUR OF SOLID FIN

## Slide 17: VELOCITY VECTOR OF SOLID FIN

## Slide 18: MODIFIED SOLID FIN
We recognize that the convective heat transfer coefficient h, in general, varies along the fin.
Its value at a point is a strong function of the fluid motion at that point.
The value of h is usually much lower at the fin base than it is at the fin tip because the fluid is surrounded by solid surfaces near the base, which disrupts it motion.
So we have modified fin by placing some holes in fin surface.

## Slide 19: MODIFIED SOLID FIN

## Slide 20: VELOCITY VECTOR FOR POROUS FIN

## Slide 21: TEMPERATURE AND VELOCITY CONTOUR

## Slide 23: EFFECT OF INCREASING HOLE DIA
10mm hole dia 15mm hole dia 20mm hole dia

## Slide 24: EFFECT OF HOLE DIA ON TEMPERATURE
23mm hole dia variable hole

## Slide 25: BASE TEMPERATURE COMPARISON
CASES | BASE TEMPERATURE | % DECREASE IN ( -)
0mm | 385.802 | 28.6
5mm | 382.78 | 27.593
10mm | 378.084 | 26.028
15mm | 375.828 | 25.27
20mm | 375.645 | 25.21
23mm | 376.534 | 25.51
variable hole | 373.755 | 24.59
CASES | BASE TEMPERATURE | 
0mm | 385.802 | 28.6
5mm | 382.78 | 27.593
10mm | 378.084 | 26.028
15mm | 375.828 | 25.27
20mm | 375.645 | 25.21
23mm | 376.534 | 25.51
variable hole | 373.755 | 24.59

## Slide 26: BAR CHART

## Slide 27: EFFECT ON HEAT TRANSTER COEFFICENT
Q = A (-)
=
For solid fin
heat flux = 240 kW/
= 385.802K
= 300K
Then = 2.79 W/

## Slide 28: TEMPERATURE DISTRIBUTION ON TOP ALONG LENGTH

## Slide 29: HEAT TRANSFER COEFF ALONG LENGTH

## Slide 30: EFFECTIVE HEAT TRANSFER COEFFICENT
CASES | EFF HEAT TRANSFER COEFFICENT () | % INCREASE IN EFFECTIVE HEAT TRANSFER COEFFICENT
5mm hole | 2.899 | 3.65
10mm hole | 3.074 | 9.88
15mm hole | 3.165 | 13.15
20mm hole | 3.173 | 13.42
23mm hole | 3.136 | 12.11
variable hole size | 3.253 | 16.28
CASES |  | % INCREASE IN EFFECTIVE HEAT TRANSFER COEFFICENT
5mm hole | 2.899 | 3.65
10mm hole | 3.074 | 9.88
15mm hole | 3.165 | 13.15
20mm hole | 3.173 | 13.42
23mm hole | 3.136 | 12.11
variable hole size | 3.253 | 16.28

## Slide 31: FUTURE SCOPE
We can also analyze the heat transfer coefficient by increasing the number of holes.

## Slide 32: REFERENCE
HEAT AND MASS TRANSFER by Yunus A Cengel and Afshin J Ghajar 4th edition ,
Tata McGraw Hill Education Private Limited ,NEW DELHI.
Golnoosh Mostafavi “NATURAL CONVECTIVEHEAT TRANSFER FROM INTRUPTED RECTANGULAR FINS” nov 2012 in university of TEHRAN.